## Slide 1: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 12 “Instruction Sets: Characteristics and Functions”.

## Slide 2: Chapter 12
Instruction Sets:
Characteristics and Functions
Notes: Much of what is discussed in this book is not readily apparent to the user or programmer of a computer. If a programmer is using a high-level language, such as Pascal or Ada, very little of the architecture of the underlying machine is visible.
One boundary where the computer designer and the computer programmer can view the same machine is the machine instruction set. From the designer’s point of view, the machine instruction set provides the functional requirements for the processor: implementing the processor is a task that in large part involves implementing the machine instruction set. The user who chooses to program in machine language (actually, in assembly language; see Appendix B) becomes aware of the register and memory structure, the types of data directly supported by the machine, and the functioning of the ALU.
A description of a computer’s machine instruction set goes a long way toward explaining the computer’s processor. Accordingly, we focus on machine instructions in this chapter and the next.

## Slide 3: Machine Instruction Characteristics
The operation of the processor is determined by the instructions it executes, referred to as machine instructions or computer instructions
The collection of different instructions that the processor can execute is referred to as the processor’s instruction set
Each instruction must contain the information required by the processor for execution
Notes: 2
The operation of the processor is determined by the instructions it executes, referred to as machine instructions or computer instructions. The collection of different instructions that the processor can execute is referred to as the processor’s instruction set.
Each instruction must contain the information required by the processor for execution.

## Slide 4: Elements of a Machine Instruction
Operation code (opcode)
Specifies the operation to be performed (ADD/IO). The operation is specified by a binary code, known as the operation code, or opcode
Source operand reference
The operation may involve one or more source operands, that is, operands that are inputs for the operation
Result operand reference
The operation may produce a result
Next instruction reference
This tells the processor where to fetch the next instruction after the execution of this instruction is complete
Ex:
ADD R1, X,Y
Opcode: Add
Source Op: X , Y
Result Op: R1
Next Instr: PC +1
Notes: • Operation code: Specifies the operation to be performed (e.g., ADD, I/O). The operation is specified by a binary code, known as the operation code, or opcode.
• Source operand reference: The operation may involve one or more source operands, that is, operands that are inputs for the operation.
• Result operand reference: The operation may produce a result.
• Next instruction reference: This tells the processor where to fetch the next instruction after the execution of this instruction is complete.

## Slide 5: Instruction Cycle
The instruction cycle is the complete process the CPU follows to execute one instruction.
Each instruction is divided into a sequence of sub cycles or phases.
Instruction Cycle = Fetch → Decode → Read → Execute
  Fetch an instruction from memory.
  Decode the instruction.
  Read the effective address from memory if the instruction has an indirect address.
  Execute the instruction.

## Slide 6
Notes: 3
Figure 12.1, which repeats Figure 3.6, shows the steps involved in instruction execution and, by implication, defines the elements of a machine instruction.
The address of the next instruction to be fetched could be either a real address or a virtual address, depending on the architecture. Generally, the distinction is transparent to the instruction set architecture. In most cases, the next instruction to be fetched immediately follows the current instruction. In those cases, there is no explicit reference to the next instruction. When an explicit reference is needed, then the main memory or virtual memory address must be supplied. The form in which that address is supplied is discussed in Chapter 13.

## Slide 7: Source and result operands can be in one of four areas:
Processor register
  A processor contains one or more registers that may be referenced by machine instructions.
  If more than one register exists each register is assigned a unique name or number and the instruction must contain the number of the desired register.
  Ex: ADD R1, R2
I/O device
  The instruction must specify the I/O module and device for the operation. Operand comes from or goes to an I/O device
Main or virtual memory
  As with next instruction references, the main or virtual memory address must be supplied.
  Virtual Address → MMU + page tables​ → Physical Address
Immediate
  The value of the operand is contained in a field in the instruction being executed.
  Ex: ADD R1, #5
Notes: 4
Source and result operands can be in one of four areas:
Main or virtual memory: As with next instruction references, the main or virtual memory address must be supplied.
Processor register: With rare exceptions, a processor contains one or more registers that may be referenced by machine instructions. If only one register exists, reference to it may be implicit. If more than one register exists, then each register is assigned a unique name or number, and the instruction must contain the number of the desired register.
Immediate: The value of the operand is contained in a field in the instruction being executed.
I/O device: The instruction must specify the I/O module and device for the operation. If memory-mapped I/O is used, this is just another main or virtual memory address.

## Slide 8: Instruction Representation
Within the computer each instruction is represented by a sequence of bits
The instruction is divided into fields, corresponding to the constituent elements of the instruction
Notes: 5
Within the computer, each instruction is represented by a sequence of bits. The instruction is divided into fields, corresponding to the constituent elements of the instruction.
A simple example of an instruction format is shown in Figure 12.2. As another example, the IAS instruction format is shown in Figure 2.2. With most instruction sets, more than one format is used. During instruction execution, an instruction is read into an instruction register (IR) in the processor. The processor must be able to extract the data from the various instruction fields to perform the required operation.
It is difficult for both the programmer and the reader of textbooks to deal with binary representations of machine instructions. Thus, it has become common practice to use a symbolic representation of machine instructions. An example of this was used for the IAS instruction set, in Table 1.1.

## Slide 9: Instruction Representation
Opcodes are represented by abbreviations called mnemonics
Examples include:
  ADD Add
  SUB Subtract
  MUL Multiply
  DIV Divide
  LOAD Load data from memory
  STOR Store data to memory
  Operands are also represented symbolically
  Each symbolic opcode has a fixed binary representation
  The programmer specifies the location of each symbolic operand
Address of
location
Register
R = R + Y
Y = 20
R = 10
R = 30
Notes: 5
Opcodes are represented by abbreviations, called mnemonics, that indicate
the operation. Common examples include
ADD Add
SUB Subtract
MUL Multiply
DIV Divide
LOAD Load data from memory
STOR Store data to memory
Operands are also represented symbolically. For example, the instruction
ADD R, Y may mean add the value contained in data location Y to the contents of register
R. In this example, Y refers to the address of a location in memory, and R refers
to a particular register. Note that the operation is performed on the contents of a
location, not on its address.
Thus, it is possible to write a machine-language program in symbolic form.
Each symbolic opcode has a fixed binary representation, and the programmer specifies
the location of each symbolic operand. For example, the programmer might
begin with a list of definitions:
X = 513
Y = 514
and so on. A simple program would accept this symbolic input, convert opcodes and
operand references to binary form, and construct binary machine instructions.
Machine-language programmers are rare to the point of nonexistence. Most
programs today are written in a high-level language or, failing that, assembly language,
which is discussed in Appendix B. However, symbolic machine language
remains a useful tool for describing machine instructions, and we will use it for that
purpose.

## Slide 10: Instruction Types
Data processing
Arithmetic instructions provide computational capabilities for processing numeric data
Logic (Boolean) instructions operate on the bits of a word as bits rather than as numbers, thus they provide capabilities for processing any other type of data the user may wish to employ
Data storage
Movement of data into or out of register and or memory locations.
Data movement
I/O instructions are needed to transfer programs and data into memory and the results of computations back out to the user
Control
Test instructions are used to test the value of a data word or the status of a computation
Branch instructions are used to branch to a different set of instructions depending on the decision made.
M - R
Test checks condition (Flag/Compare)
Branch jump based on results.
Notes: 6
A computer should have a set of instructions that allows the user to formulate any data processing task. Another way to view it is to consider the capabilities of a high-level programming language. Any program written in a high-level language must be translated into machine language to be executed. Thus, the set of machine instructions must be sufficient to express any of the instructions from a high-level language. With this in mind we can categorize instruction types as follows:
Data processing: Arithmetic and logic instructions
Data storage: Movement of data into or out of register and or memory
locations
Data movement: I/O instructions
Control: Test and branch instructions
Arithmetic instructions provide computational capabilities for processing numeric data. Logic (Boolean) instructions operate on the bits of a word as bits rather than as numbers; thus, they provide capabilities for processing any other type of data the user may wish to employ. These operations are performed primarily on data in processor registers. Therefore, there must be memory instructions for moving data between memory and the registers. I/O instructions are needed to transfer programs and data into memory and the results of computations back out to the user. Test instructions are used to test the value of a data word or the status of a computation. Branch instructions are then used to branch to a different set of instructions depending on the decision made.

## Slide 11: Number of Addresses/Operands
Arithmetic and logic instructions will require the most operands.
  Unary – one source operand (accumulator) – Ex: INC A
  Binary – two source operand (general-purpose registers) – Ex: ADD A,B
Four address references
  Two source operands
  One destination operand
  Address of the next instruction
  Advantages: Fewer addresses per instruction result in instructions that are:
  More primitive
  Requiring a less complex processor
  Shorter instruction length
  Disadvantages: these instruction results in
  Longer and complex program
  Longer execution times
ADD | X | Y | Z | #500

## Slide 12
Notes: 7
One of the traditional ways of describing processor architecture is in terms of the
number of addresses contained in each instruction. This dimension has become less
significant with the increasing complexity of processor design. Nevertheless, it is useful
at this point to draw and analyze this distinction.
What is the maximum number of addresses one might need in an instruction?
Evidently, arithmetic and logic instructions will require the most operands.
Virtually all arithmetic and logic operations are either unary (one source
operand) or binary (two source operands). Thus, we would need a maximum of
two addresses to reference source operands. The result of an operation must be
stored, suggesting a third address, which defines a destination operand. Finally,
after completion of an instruction, the next instruction must be fetched, and its
address is needed.
This line of reasoning suggests that an instruction could plausibly be required
to contain four address references: two source operands, one destination operand,
and the address of the next instruction. In most architectures, many instructions
have one, two, or three operand addresses, with the address of the next instruction
being implicit (obtained from the program counter). Most architectures also have
a few special-purpose instructions with more operands. For example, the load and
store multiple instructions of the ARM architecture, described in Chapter 13, designate
up to 17 register operands in a single instruction.
Figure 12.3 compares typical one, two, and three address instructions that
could be used to compute Y = (A – B)/[C + (D * E)]. With three addresses, each instruction specifies two source operand locations and a destination operand location. Because we choose not to alter the value of any of the operand locations, a temporary location, T, is used to store some intermediate results. Note that there are four instructions and that the original expression had five operands.
Three-address instruction formats are not common because they require a relatively long instruction format to hold the three address references. With two- address instructions, and for binary operations, one address must do double duty as both an operand and a result. Thus, the instruction SUB Y, B carries out the calculation Y - B and stores the result in Y. The two-address format reduces the space requirement but also introduces some awkwardness. To avoid altering the value of an operand, a MOVE instruction is used to move one of the values to a result or temporary location before performing the operation. Our sample program expands to six instructions.
Simpler yet is the one-address instruction. For this to work, a second address must be implicit. This was common in earlier machines, with the implied address being a processor register known as the accumulator (AC). The accumulator contains one of the operands and is used to store the result. In our example, eight instructions are needed to accomplish the task.
It is, in fact, possible to make do with zero addresses for some instructions. Zero-address instructions are applicable to a special memory organization called a stack. A stack is a last-in-first-out set of locations. The stack is in a known location and, often, at least the top two elements are in processor registers. Thus, zero-address instructions would reference the top two stack elements. Stacks are described in Appendix I. Their use is explored further later in this chapter and in Chapter 13.

## Slide 13
Table 12.1
Utilization of Instruction Addresses
(Non branching Instructions)
Zero-address instructions are applicable to a special memory organization called a stack. A stack is a last-in-first-out set of locations. The stack is in a known location and, often, at least the top two elements are in processor registers. Thus, zero-address instructions would reference the top two stack elements.
Notes: 8
Table 12.1 summarizes the interpretations to be placed on instructions with zero, one, two, or three addresses. In each case in the table, it is assumed that the address of the next instruction is implicit, and that one operation with two source operands and one result operand is to be performed.
The number of addresses per instruction is a basic design decision. Fewer addresses per instruction result in instructions that are more primitive, requiring a less complex processor. It also results in instructions of shorter length. On the other hand, programs contain more total instructions, which in general results in longer execution times and longer, more complex programs. Also, there is an important threshold between one-address and multiple-address instructions. With one-address instructions, the programmer generally has available only one general-purpose register, the accumulator. With multiple-address instructions, it is common to have multiple general-purpose registers. This allows some operations to be performed
solely on registers. Because register references are faster than memory references, this speeds up execution. For reasons of flexibility and ability to use multiple registers, most contemporary machines employ a mixture of two- and three-address instructions.
The design trade-offs involved in choosing the number of addresses per instruction are complicated by other factors. There is the issue of whether an address references a memory location or a register. Because there are fewer registers, fewer bits are needed for a register reference. Also, as we shall see in Chapter 13, a machine may offer a variety of addressing modes, and the specification of mode takes one or more bits. The result is that most processor designs involve a variety of instruction formats.

## Slide 14: Instruction Set Design
Very complex because it affects so many aspects of the computer system
Defines many of the functions performed by the processor
Programmer’s means of controlling the processor
Fundamental design issues:
Operation repertoire
How many and which operations to provide and how complex operations should be
Data types
The various types of data upon which operations are performed
Instruction format
Instruction length in bits, number of addresses, size of various fields, etc.
Registers
Number of processor registers that can be referenced by instructions and their use
Addressing
The mode or modes by which the address of an operand is specified
Notes: 9
One of the most interesting, and most analyzed, aspects of computer design is instruction set design. The design of an instruction set is very complex because it affects so many aspects of the computer system. The instruction set defines many of the functions performed by the processor and thus has a significant effect on the implementation of the processor. The instruction set is the programmer’s means of controlling the processor. Thus, programmer requirements must be considered in designing the instruction set.
It may surprise you to know that some of the most fundamental issues relating to the design of instruction sets remain in dispute. Indeed, in recent years, the level of disagreement concerning these fundamentals has actually grown. The most important of these fundamental design issues include the following:
Operation repertoire: How many and which operations to provide, and how complex operations should be
Data types: The various types of data upon which operations are performed
Instruction format: Instruction length (in bits), number of addresses, size of
various fields, and so on
Registers: Number of processor registers that can be referenced by instructions, and their use
Addressing: The mode or modes by which the address of an operand is specified
These issues are highly interrelated and must be considered together in designing an instruction set. This book, of course, must consider them in some sequence, but an attempt is made to show the interrelationships.
Because of the importance of this topic, much of Part Three is devoted to
instruction set design. Following this overview section, this chapter examines data
types and operation repertoire. Chapter 13 examines addressing modes (which
includes a consideration of registers) and instruction formats. Chapter 15 examines
the reduced instruction set computer (RISC). RISC architecture calls into question
many of the instruction set design decisions traditionally made in commercial
computers.

## Slide 15: Types of Operands
Addresses
Numbers
Characters
Logical Data
Notes: 14
Machine instructions operate on data. The most important general categories of data are
Addresses
Numbers
Characters
Logical data
We shall see, in discussing addressing modes in Chapter 13, that addresses are, in fact, a form of data. In many cases, some calculation must be performed on the operand reference in an instruction to determine the main or virtual memory address. In this context, addresses can be considered to be unsigned integers.
Other common data types are numbers, characters, and logical data, and each of these is briefly examined in this section. Beyond that, some machines define specialized data types or data structures. For example, there may be machine operations that operate directly on a list or a string of characters.

## Slide 16: Numbers
All machine languages include numeric data types
Numbers stored in a computer are limited:
  Limit to the magnitude of numbers representable on a machine
  In the case of floating-point numbers, a limit to their precision
  Three types of numerical data are common in computers:
  Binary integer or binary fixed point
  Binary floating point
  Decimal
  Packed decimal
  Each decimal digit is represented by a 4-bit code with two digits stored per byte
  To form numbers 4-bit codes are strung together, usually in multiples of 8 bits. Ex: the code for 246 is 0000 0010 0100 0110
Notes: All machine languages include numeric data types. Even in nonnumeric data processing, there is a need for numbers to act as counters, field widths, and so forth. An important distinction between numbers used in ordinary mathematics and numbers stored in a computer is that the latter are limited. This is true in two senses. First, there is a limit to the magnitude of numbers representable on a machine and second, in the case of floating-point numbers, a limit to their precision. Thus, the programmer is faced with understanding the consequences of rounding, overflow, and underflow.
Three types of numerical data are common in computers:
  Binary integer or binary fixed point
  Binary floating point
  Decimal
  We examined the first two in some detail in Chapter 10. It remains to say a few words about decimal numbers.
  Although all internal computer operations are binary in nature, the human users of the system deal with decimal numbers. Thus, there is a necessity to convert from decimal to binary on input and from binary to decimal on output. For applications in which there is a great deal of I/O and comparatively little, comparatively simple computation, it is preferable to store and operate on the numbers in decimal form. The most common representation for this purpose is packed decimal.
With packed decimal, each decimal digit is represented by a 4-bit code, in the obvious way, with two digits stored per byte. Thus, 0 = 000, 1 = 0001, c, 8 = 1000, and 9 = 1001. Note that this is a rather inefficient code because only 10 of 16 possible 4-bit values are used. To form numbers, 4-bit codes are strung together, usually in multiples of 8 bits. Thus, the code for 246 is 0000 0010 0100 0110. This code is clearly less compact than a straight binary representation, but it avoids the con- version overhead. Negative numbers can be represented by including a 4-bit sign digit at either the left or right end of a string of packed decimal digits. Standard sign values are 1100 for positive (+) and 1101 for negative (-).
Many machines provide arithmetic instructions for performing operations directly on packed decimal numbers. The algorithms are quite similar to those described in Section 9.3 but must take into account the decimal carry operation.

## Slide 17: Characters
A common form of data is text or character strings
Textual data in character form cannot be easily stored or transmitted by data processing and communications systems because they are designed for binary data
Most commonly used character code is the International Reference Alphabet (IRA)
  Referred to in the United States as the American Standard Code for Information Interchange (ASCII)
  Ex: A (65), a(97), 0(48), @(64)
  Another code used to encode characters is the Extended Binary Coded Decimal Interchange Code (EBCDIC)
  EBCDIC is used on IBM mainframes
Notes: A common form of data is text or character strings. While textual data are most convenient for human beings, they cannot, in character form, be easily stored or transmitted by data processing and communications systems. Such systems are designed for binary data. Thus, a number of codes have been devised by which characters are represented by a sequence of bits. Perhaps the earliest common example of this is the Morse code. Today, the most commonly used character code in the International Reference Alphabet (IRA), referred to in the United States as the American Standard Code for Information Interchange (ASCII; see Appendix F). Each character in this code is represented by a unique 7-bit pattern; thus, 128 different characters can be represented. This is a larger number than is necessary to represent printable characters, and some of the patterns represent control characters. Some of these control characters have to do with controlling the printing of characters on a page. Others are concerned with communications procedures. IRA-encoded characters are almost always stored and transmitted using 8 bits per character. The eighth bit may be set to 0 or used as a parity bit for error detection. In the latter case, the bit is set such that the total number of binary 1s in each octet is always odd (odd parity) or always even (even parity).
Note in Table H.1 (Appendix H) that for the IRA bit pattern 011XXXX, the digits 0 through 9 are represented by their binary equivalents, 0000 through 1001, in the rightmost 4 bits. This is the same code as packed decimal. This facilitates con- version between 7-bit IRA and 4-bit packed decimal representation.
Another code used to encode characters is the Extended Binary Coded Decimal Interchange Code (EBCDIC). EBCDIC is used on IBM mainframes. It is an 8-bit code. As with IRA, EBCDIC is compatible with packed decimal. In the case of EBCDIC, the codes 11110000 through 11111001 represent the digits 0 through 9.

## Slide 18: Logical Data
An n-bit unit consisting of n 1-bit items of data, each item having the value 0 or 1
Two advantages to bit-oriented view:
  Memory can be used most efficiently for storing an array of Boolean or binary data items in which each item can take on only the values 1 (true) and 0 (false)
  To manipulate the bits of a data item
    If floating-point operations are implemented in software, we need to be able to shift significant bits in some operations
    To convert from IRA to packed decimal, we need to extract the rightmost 4 bits of each byte
Notes: Normally, each word or other addressable unit (byte, halfword, and so on) is treated as a single unit of data. It is sometimes useful, however, to consider an n-bit unit as consisting of n 1-bit items of data, each item having the value 0 or 1. When data are viewed this way, they are considered to be logical data.
There are two advantages to the bit-oriented view. First, we may sometimes wish to store an array of Boolean or binary data items, in which each item can take on only the values 1 (true) and 0 (false). With logical data, memory can be used most efficiently for this storage. Second, there are occasions when we wish to manipulate the bits of a data item. For example, if floating-point operations are implemented in software, we need to be able to shift significant bits in some operations. Another example: To convert from IRA to packed decimal, we need to extract the rightmost 4 bits of each byte.
Note that, in the preceding examples, the same data are treated sometimes as logical and other times as numerical or text. The “type” of a unit of data is deter- mined by the operation being performed on it. While this is not normally the case in high-level languages, it is almost always the case with machine language.

## Slide 19: Intel x86 and ARM Data Types
Data type: A specific kind of data that a processor can operate on.
Examples:
  Integer (byte , word, double word)
  Floating-point (single, double precision)
  Characters and Boolean
  Purpose: Defines how much memory is used and how data is interpreted.

## Slide 20: Intel x86 Architecture Overview
Developed by Intel; dominant in PCs and Servers.
CISC (Complex Instruction Set Computing) architecture.
Rich set of instructions and varied data sizes.
Backward compatible supports legacy 16 – bit and 32 – bit modes.
Integers: Signed represent both positive and negative values whereas unsigned represents only non-negative values.
Floating data types are handled by X87 FPU and used for scientific and graphics computations.
Data Alignment in memory makes the faster performance than unaligned access (e.g., 4 byte – 0,4,8,12,16….)

## Slide 21
Data Type | Size | Name | Description
Integer | 8-bit | Byte | Basic unit of data (small integer)
Integer | 16-bit | Word | Standard data size in early x86
Integer | 32-bit | Double Word | Common integer size in modern systems
Integer | 64-bit | Quad Word | Large integer for high precision
Floating | 80-bit | Ten Bytes | Extended precision floating-point (x87 FPU)
Intel x86 Data Types

## Slide 22
Table 12.2
x86
Data Types
Notes: The x86 can deal with data types of 8 (byte), 16 (word), 32 (doubleword), 64 (quad- word), and 128 (double quadword) bits in length. To allow maximum flexibility in data structures and efficient memory utilization, words need not be aligned at even- numbered addresses; doublewords need not be aligned at addresses evenly divisible by 4; and quadwords need not be aligned at addresses evenly divisible by 8; and so on. However, when data are accessed across a 32-bit bus, data transfers take place in units of doublewords, beginning at addresses divisible by 4. The processor converts the request for misaligned values into a sequence of requests for the bus transfer. As with all of the Intel 80x86 machines, the x86 uses the little-endian style; that is, the least significant byte is stored in the lowest address (see Appendix 12A for a discussion of endianness).
The byte, word, doubleword, quadword, and double quadword are referred to as general data types. In addition, the x86 supports an impressive array of specific data types that are recognized and operated on by particular instructions. Table 12.2 summarizes these types.

## Slide 23
Notes: Figure 12.4 illustrates the x86 numerical data types. The signed integers are in twos complement representation and may be 16, 32, or 64 bits long. The floating- point type actually refers to a set of types that are used by the floating-point unit and operated on by floating-point instructions. The three floating-point representations conform to the IEEE 754 standard.

## Slide 24: Single-Instruction-Multiple-Data (SIMD) Data Types
Introduced to the x86 architecture as part of the extensions of the instruction set to optimize performance of multimedia applications
These extensions include MMX (multimedia extensions) and SSE (streaming SIMD extensions)
Data types:
  Packed byte and packed byte integer
  Packed word and packed word integer
  Packed doubleword and packed doubleword integer
  Packed quadword and packed quadword integer
  Packed single-precision floating-point and packed double-precision floating-point
Notes: 16
The packed SIMD (single-instruction-multiple-data) data types were introduced to the x86 architecture as part of the extensions of the instruction set to optimize performance of multimedia applications. These extensions include MMX (multimedia extensions) and SSE (streaming SIMD extensions). The basic concept is that multiple operands are packed into a single referenced memory item and that these multiple operands are operated on in parallel. The data types are as follows:
Packed byte and packed byte integer: Bytes packed into a 64-bit quadword or 128-bit double quadword, interpreted as a bit field or as an integer
Packed word and packed word integer: 16-bit words packed into a 64-bit quad- word or 128-bit double quadword, interpreted as a bit field or as an integer
• Packed doubleword and packed doubleword integer: 32-bit doublewords packed into a 64-bit quadword or 128-bit double quadword, interpreted as a bit field or as an integer
• Packed quadword and packed qaudword integer: Two 64-bit quadwords packed into a 128-bit double quadword, interpreted as a bit field or as an integer
• Packed single-precision floating-point and packed double-precision floating- point: Four 32-bit floating-point or two 64-bit floating-point values packed into a 128-bit double quadword

## Slide 25: SISD/SIMD/MISD/MIMD

## Slide 26: ARM Architecture Overview
ARM (Advanced RISC Machine) – RISC Architecture
Focused on simplicity and power efficiency.
Common in mobile and embedded systems.
Uses load/store architecture – all data operations use registers.
ARM usually enforce natural alignment.
ARM Supports:
  Integer data types (8 bit to 64 bit)
  Floating – point data types (32 bit to 64 bit)
  Vector (SIMD) data types for NEON instructions
  Boolean data (true/false)

## Slide 27: ARM Data Types
ARM processors support data types of:
8 (byte) – can be stored at any location.
16 (halfword) – must be aligned, begin at even address {0,2,4,6..}
32 (word) bits in length – must be aligned, begin at multiple of 4 {0,4,5,..}
Alignment checking
When the appropriate control bit is set, a data abort signal indicates an alignment fault for attempting unaligned access
Unaligned access
When this option is enabled, the processor uses one or more memory accesses to generate the required transfer of adjacent bytes transparently to the programmer
For all three data types an unsigned interpretation is supported in which the value represents an unsigned, nonnegative integer
All three data types can also be used for twos complement signed integers
After loading the data from memory, the data must be extended into 32 bits bcz register size will be 32 bits.
Notes: ARM processors support data types of 8 (byte), 16 (halfword), and 32 (word) bits in length. Normally, halfword access should be halfword aligned and word accesses should be word aligned. For nonaligned access attempts, the architecture supports three alternatives.
• Default case:
– The address is treated as truncated, with address bits[1:0] treated as zero for word accesses, and address bit[0] treated as zero for halfword accesses.
– Load single word ARM instructions are architecturally defined to rotate right the word-aligned data transferred by a non word-aligned address one, two, or three bytes depending on the value of the two least significant address bits.
• Alignment checking: When the appropriate control bit is set, a data abort signal indicates an alignment fault for attempting unaligned access.
• Unaligned access: When this option is enabled, the processor uses one or more memory accesses to generate the required transfer of adjacent bytes transparently to the programmer.
For all three data types (byte, halfword, and word) an unsigned interpretation is supported, in which the value represents an unsigned, nonnegative integer. All three data types can also be used for twos complement signed integers.
The majority of ARM processor implementations do not provide floating- point hardware, which saves power and area. If floating-point arithmetic is required in such processors, it must be implemented in software. ARM does support an optional floating-point coprocessor that supports the single- and double-precision floating point data types defined in IEEE 754.

## Slide 28: Types of Operations
The number of different opcodes varies widely from machine to machine. However, the same general types of operations are found on all machines. A useful and typical categorization is the following: Data transfer, Arithmetic, Logical, Conversion, I/O, System control, and Transfer of control

## Slide 29
Table 12.3
Common Instruction Set Operations
(page 1 of 2)
(Table can be found on page
426 in textbook.)
Notes: 18
The number of different opcodes varies widely from machine to machine. However, the same general types of operations are found on all machines. A useful and typical categorization is the following:
Data transfer
Arithmetic
Logical
Conversion
I/O
System control
Transfer of control
Table 12.3 (based on [HAYE98]) lists common instruction types in each category.

## Slide 30
Table 12.3
Common Instruction Set Operations
(page 2 of 2)
(Table can be found on page
426 in textbook.)
Notes: 18
Table 12.3, page 2 of 2

## Slide 31: Examples:
Type | Example | Description
Data Transfer Instructions | MOV A, B | Copies data from one register/memory location to another without changing it.
Arithmetic Instructions | ADD A, B | Performs mathematical operations like addition, subtraction, multiplication, or division.
Logical Instructions | AND A, B | Performs bitwise logical operations (AND, OR, NOT, XOR) on binary data.
Conversion Instructions | CONVERT A, INT_TO_FLOAT | Converts data from one format/type to another (e.g., integer to float, BCD to binary).
I/O (Input/Output) Instructions | IN A, KEYBOARD | Transfers data between CPU and external devices (keyboard, screen, printer, etc.).
System Control Instructions | HLT | Controls the CPU/system state (start, stop, enable/disable interrupts).
Transfer of Control Instructions | JMP LABEL | Changes the normal execution flow by jumping to another instruction or function.

## Slide 32
Table 12.4
Processor Actions for Various Types of Operations
(Table can be found on page 427 in textbook.)
Notes: This section provides a brief survey of these various types of operations, together with a brief discussion of the actions taken by the processor to execute a particular type of operation (summarized in Table 12.4). The latter topic is examined in more detail in Chapter 14.

## Slide 33: x86 Operation Types
The x86 provides a complex array of operation types including a number of specialized instructions
The intent was to provide tools for the compiler writer to produce optimized machine language translation of high-level language programs
Provides four instructions to support procedure call/return:
  CALL : CALL FUNC, PUSH return_address - JUMP FUNC
  ENTER: ENTER 20, 0, 20 = space for local variables
  LEAVE: Reverses ENTER (destroys stack frame)
  RETURN: Returns control to calling function, POP return_address, JUMP return_address
When a new procedure is called the following must be performed upon entry to the new procedure:
  Push the return point on the stack
  Push the current frame pointer on the stack
  Copy the stack pointer as the new value of the frame pointer
  Adjust the stack pointer to allocate a frame
Notes: The x86 provides a complex array of operation types, including a number of specialized instructions. The intent was to provide tools for the compiler writer to produce optimized machine language translation of high-level language programs. Table 12.8 lists the types and gives examples of each. Most of these are the conventional instructions found in most machine instruction sets, but several types of instructions are tailored to the x86 architecture and are of particular interest. Appendix A of [CART06] lists the x86 instructions, together with the operands
for each and the effect of the instruction on the condition codes. Appendix B of
the NASM assembly language manual [NASM12] provides a more detailed description
of each x86 instruction. Both documents are available at box.com/COA10e.
The x86 provides four instructions to support
procedure call/return: CALL, ENTER, LEAVE, RETURN. It will be instructive to
look at the support provided by these instructions. Recall from Figure 12.10 that a
common means of implementing the procedure call/return mechanism is via the use
of stack frames. When a new procedure is called, the following must be performed
upon entry to the new procedure:
■ Push the return point on the stack.
■ Push the current frame pointer on the stack.
■ Copy the stack pointer as the new value of the frame pointer.
■ Adjust the stack pointer to allocate a frame.
The CALL instruction pushes the current instruction pointer value onto the stack
and causes a jump to the entry point of the procedure by placing the address of the
entry point in the instruction pointer. In the 8088 and 8086 machines, the typical
procedure began with the sequence
PUSH EBP
MOV EBP, ESP
SUB ESP, space_for_locals
where EBP is the frame pointer and ESP is the stack pointer. In the 80286 and later
machines, the ENTER instruction performs all the aforementioned operations in a
single instruction.
The ENTER instruction was added to the instruction set to provide direct support
for the compiler. The instruction also includes a feature for support of what are
called nested procedures in languages such as Pascal, COBOL, and Ada (not found
in C or FORTRAN). It turns out that there are better ways of handling nested procedure
calls for these languages. Furthermore, although the ENTER instruction
saves a few bytes of memory compared with the PUSH, MOV, SUB sequence (4
bytes versus 6 bytes), it actually takes longer to execute (10 clock cycles versus 6
clock cycles). Thus, although it may have seemed a good idea to the instruction set
designers to add this feature, it complicates the implementation of the processor
while providing little or no benefit. We will see that, in contrast, a RISC approach
to processor design would avoid complex instructions such as ENTER and might
produce a more efficient implementation with a sequence of simpler instructions.
Another set of specialized instructions deals with memory
segmentation. These are privileged instructions that can only be executed from the
operating system. They allow local and global segment tables (called descriptor
tables) to be loaded and read, and for the privilege level of a segment to be checked
and altered.
The special instructions for dealing with the on-chip cache were discussed in Chapter 4.

## Slide 34
Table 12.8
x86 Status Flags
Status Bit | Name | Description | Example
CF | Carry Flag | Indicates a carry or borrow out of the most significant bit after an arithmetic operation. Also affected by shift/rotate operations. | 11111111 + 00000001 = 1 00000000 → CF = 1
PF | Parity Flag | Indicates parity (even/odd) of the least significant byte of the result. PF = 1 if even parity. | 00000000 → PF = 1 (even parity)
AF | Auxiliary Carry Flag | Indicates carry/borrow between lower nibble (4 bits) and upper nibble in 8-bit operations. Used in BCD arithmetic. | 0000 1111 + 0000 0001 → AF = 1
ZF | Zero Flag | Set to 1 if the result of an operation is zero. | 5 - 5 = 0 → ZF = 1
SF | Sign Flag | Indicates sign of result (1 = negative, 0 = positive). | -5 result → SF = 1
OF | Overflow Flag | Indicates arithmetic overflow in signed (2’s complement) operations. | 127 + 1 = -128 (overflow) → OF = 1
Notes: 27
Status flags are bits in special registers
that may be set by certain operations and used in conditional branch instructions.
The term condition code refers to the settings of one or more status flags. In the
x86 and many other architectures, status flags are set by arithmetic and compare
operations. The compare operation in most languages subtracts two operands, as
does a subtract operation. The difference is that a compare operation only sets
status flags, whereas a subtract operation also stores the result of the subtraction
in the destination operand. Some architectures also set status flags for data transfer
instructions.
Table 12.8 lists the status flags used on the x86. Each flag, or combinations
of these flags, can be tested for a conditional jump.

## Slide 35
Table 12.9
x86
Condition Codes
for Conditional Jump
and
SET Instructions
(Table can be found on page 440 in the textbook.)
Notes: Table 12.9 shows the condition codes (combinations of status flag values) for which
conditional jump opcodes have been defined.
Several interesting observations can be made about this list. First, we may
wish to test two operands to determine if one number is bigger than another. But
this will depend on whether the numbers are signed or unsigned. For example, the
8-bit number 11111111 is bigger than 00000000 if the two numbers are interpreted
as unsigned integers (255 > 0) but is less if they are considered as 8-bit twos complement
numbers ( - 1< 0). Many assembly languages therefore introduce two sets
of terms to distinguish the two cases: If we are comparing two numbers as signed
integers, we use the terms less than and greater than; if we are comparing them as
unsigned integers, we use the terms below and above.
A second observation concerns the complexity of comparing signed integers.
A signed result is greater than or equal to zero if (1) the sign bit is zero and there is
no overflow (S = 0 AND O = 0), or (2) the sign bit is one and there is an overflow.
A study of Figure 10.4 should convince you that the conditions tested for the various
signed operations are appropriate.

## Slide 36
Note: If an instruction supports multiple data types [byte (B), word (W), doubleword (D), quadword (Q)], the data types are indicated in brackets.
Table 12.10
MMX Instruction Set
(Table can be found on page 442 in the textbook.)
Notes: Table 12.10 lists the MMX instruction set. Most of the instructions involve
parallel operation on bytes, words, or doublewords. For example, the PSLLW
instruction performs a left logical shift separately on each of the four words in the
packed word operand; the PADDB instruction takes packed byte operands as input
and performs parallel additions on each byte position independently to produce a
packed byte output.
One unusual feature of the new instruction set is the introduction of saturation
arithmetic for byte and 16-bit word operands. With ordinary unsigned arithmetic,
when an operation overflows (i.e., a carry out of the most significant bit), the
extra bit is truncated. This is referred to as wraparound, because the effect of the
truncation can be, for example, to produce an addition result that is smaller than the
two input operands.

## Slide 37: ARM Operation Types
Load and store instructions
Branch instructions
Data-processing instructions
Multiply instructions
Parallel addition and subtraction instructions
Extend instructions
Status register access instructions
Notes: The ARM architecture provides a large collection of operation types. The following
are the principal categories:
Load and store instructions: In the ARM architecture, only load and store instructions access memory locations; arithmetic and logical instructions are performed only on registers and immediate values encoded in the instruction. This limitation is characteristic of RISC design and it is explored further in Chapter 15. The ARM architecture supports two broad types of instruction that load or store the value of a single register, or a pair of registers, from or to memory: (1) load or store a 32-bit word or an 8-bit unsigned byte, and (2) load or store a 16-bit unsigned halfword, and load and sign extend a 16-bit halfword or an 8-bit byte.
Branch instructions: ARM supports a branch instruction that allows a conditional branch forwards or backwards up to 32 MB. As the program counter is one of the general-purpose registers (R15), a branch or jump can also be generated by writing a value to R15. A subroutine call can be performed by a variant of the standard branch instruction. As well as allowing a branch forward or backward up to 32 MB, the Branch with Link (BL) instruction preserves the address of the instruction after the branch (the return address) in the LR (R14). Branches are determined by a 4-bit condition field in the instruction.
Data-processing instructions: This category includes logical instructions (AND, OR, XOR), add and subtract instructions, and test and compare instructions.
Multiply instructions: The integer multiply instructions operate on word or halfword operands and can produce normal or long results. For example, there is a multiply instruction that takes two 32-bit operands and produces a 64-bit result.
Parallel addition and subtraction instructions: In addition to the normal data processing and multiply instructions, there are a set of parallel addition and subtraction instructions, in which portions of two operands are operated on in parallel. For example, ADD16 adds the top halfwords of two registers to form the top halfword of the result and adds the bottom halfwords of the same two registers to form the bottom halfword of the result. These instructions are useful in image processing applications, similar to the x86 MMX instructions.
Extend instructions: There are several instructions for unpacking data by sign or zero extending bytes to halfwords or words, and halfwords to words.
Status register access instructions: ARM provides the ability to read and also to write portions of the status register.

## Slide 38
Table 12.11
ARM Conditions for Conditional Instruction Execution
(Table can be found on
Page 445 in the textbook.)
Notes: The ARM architecture defines four condition flags that are stored in the program status register: N, Z, C, and V (Negative, Zero, Carry and Overflow), with meanings essentially the same as the S, Z, C, and V flags
in the x86 architecture. These four flags constitute a condition code in ARM. Table 12.11 shows the combination of conditions for which conditional execution is defined.
There are two unusual aspects to the use of condition codes in ARM:
All instructions, not just branch instructions, include a condition code field, which means that virtually all instructions may be conditionally executed. Any combination of flag settings except 1110 or 1111 in an instruction’s condition code field signifies that the instruction will be executed only if the condition is met.
All data processing instructions (arithmetic, logical) includes an S bit that signifies whether the instruction updates the condition flags.
The use of conditional execution and conditional setting of the condition flags
helps in the design of shorter programs that use less memory. On the other hand, all instructions include 4 bits for the condition code, so there is a trade-off in that fewer bits in the 32-bit instruction are available for opcode and operands. Because the ARM is a RISC design that relies heavily on register addressing, this seems to be a reasonable trade-off.

## Slide 39: Summary
Machine instruction characteristics
  Elements of a machine instruction
  Instruction representation
  Instruction types
  Number of addresses
  Instruction set design
Types of operands
  Numbers
  Characters
  Logical data
  Intel x86 and ARM data types
  Types of operations
  Data transfer
  Arithmetic
  Logical
  Conversion
  Input/output
  System control
  Transfer of control
  Intel x86 and ARM operation types
Chapter 12
Instruction Sets:
Characteristics and Functions
Notes: Chapter 12 summary.